## Slide 1: Number Systems

## Slide 2
Common Number Systems
System | Base | Symbols | Used by humans? | Used in computers?
Decimal | 10 | 0, 1, … 9 | Yes | No
Binary | 2 | 0, 1 | No | Yes
Octal | 8 | 0, 1, … 7 | No | No
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No

## Slide 3
Quantities/Counting (1 of 3)
Decimal | Binary | Octal | Hexa- decimal
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
p. 33

## Slide 4
Quantities/Counting (2 of 3)
Decimal | Binary | Octal | Hexa- decimal
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 5
Decimal | Binary | Octal | Hexa- decimal
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15
22 | 10110 | 26 | 16
23 | 10111 | 27 | 17
Etc.
Quantities/Counting (3 of 3)

## Slide 6
Conversion Among Bases
The possibilities:
Hexadecimal
Decimal
Octal
Binary

## Slide 7
Quick Example
2510 = 110012 = 318 = 1916
Base

## Slide 8
Decimal to Binary
Technique
  Divide by two, keep track of the remainder
  First remainder is bit 0 (LSB, least-significant bit)
  Second remainder is bit 1
  Etc.

## Slide 9
Example
12510 = ?2
2 125 62 1
2 31 0
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12510 = 11111012

## Slide 10: the most significant bit (MSB)
In computing, the most significant bit (MSB, also called the high-order bit) is the bit position in a binary number having the greatest value. The MSB is sometimes referred to as the left-most bit due to the convention in positional notation of writing more significant digits further to the left.

## Slide 11: Exercise
Convert decimal 25 to a binary number

## Slide 12
Binary to Decimal
Technique
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 13
Example
1010112 => 1 x 20 = 1 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4310
Bit “0”

## Slide 14: Exercise
Convert 111001 binary number to a decimal

## Slide 15: Decimal to Hexadecimal
Technique
  Divide by 16
  Keep track of the remainder

## Slide 16: Example
123410 = ?16
123410 = 4D216
16 1234
77 2
16
4 13 = D
16
0 4

## Slide 17: Exercise
Convert decimal 2468 to a hex number

## Slide 18
Hexadecimal to Decimal
Technique
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 19: Exercise
Convert hex number to a decimal

## Slide 20: Hexadecimal to Binary
Technique
  Convert each hexadecimal digit to a 4-bit equivalent binary representation

## Slide 21: Example
10AF16 = ?2
1 0 A F
0001 0000 1010 1111
10AF16 = 00010000101011112

## Slide 22: Binary to Hexadecimal
Technique
  Group bits in fours, starting on right
  Convert to hexadecimal digits

## Slide 23: Example
10101110112 = ?16
10 1011 1011
B B
10101110112 = 2BB16

## Slide 24: Example
/ 230 =
In the lab… 1. Double click on My Computer 2. Right click on C: 3. Click on Properties

## Slide 25: Home Work ?
Convert the following Decimal numbers to binary
Convert the following binary numbers to decimal
25
32
64
128
255
511
111111
100000
11
111
10000
101010

## Slide 26
Exercise 1.3